Pre-Calculus

Test 1 Extra Credit Problems

Worksheet

- Height of a kite – A person flying a kite holds the string 4 feet above ground level. The string of the kite is taut and makes an angle of 60° with the horizontal. Approximate the height of the kite above level ground if 500 feet of string is payed out.

437 ft

- Surveying – From a point 11 meters above level ground, a surveyor measures the angle of depression of an object on the ground as 68°. Approximate the distance from the object to the point on the ground directly beneath the surveyor.

6.06 ft

- Radio antenna – A guy wire is attached to the top of a radio antenna and to a point on horizontal ground that is 40.0 meters from the base of the antenna. If the wire makes an angle of 58°20’ with the ground, approximate the length of the wire.

76.1 m

- Meteorological calculations – To measure the height h of a cloud cover, a meteorology student directs a spotlight vertically upward from the ground. From a point P on level ground that is d meters from the spotlight, the angle of elevation θ of the light image on clouds is then measured.

  - Express h in terms of d and θ.

h = d tan θ

  - Approximate h if d = 1000 m and θ = 59°.

1664.3 m

- Airplane takeoff – An airplane takes off at a 10° angle and travels at the rate of 250 ft/sec. Approximately how long does it take the airplane to reach an altitude of 15,000 feet?

345.5 sec or 5.6 min

- Designing a draw bridge – A draw bridge is 150 feet long when stretched across a river. As shown in the figure, the two sections of the bridge can be rotated upward through an angle o f 35°.

  - If the water level is 15 feet below the closed bridge, find the distance d between the end of a section and the water level when the bridge is fully open.

58 ft

  - Approximately how far apart are the ends of the two sections when the bridge is fully opened, as shown in the figure?

27 ft

- Designing a water slide – Show in the figure is part of a design for a water slide. Find the total length of the slide to the nearest foot.

108 ft

- Constructing a ramp – A builder wishes to construct a ramp 24 feet long that rises to a height of 5.0 feet above level ground. Approximate the angle that the ramp should make with the horizontal.

12.02°

- The Pentagon’s ground area – The Pentagon is the largest office building in the world in terms of ground area. The perimeter of the building has the shape of a regular pentagon with each side of length 921 feet. Find the area enclosed by the perimeter of the building.

1,459,379 ft2

# Text boxes

35°

150’

d

35°

15’

35°

15’

25°

100’